SUNRISE EVALUATION EXAM FORM 4 - 2022

FORM 4 PHYSICS  MARKING SCHEME

Paper 2

SECTION A

- Primary cells cannot be recharged after use while secondary cells can be recharged after use.

- Λ = 4.0mm       V = fλ

f = 1/2x10-3 = 500Hz

1m = 1000mm = 4.0 x 10-3m/s

V = 500 x 4 x 10-3 = 2.0m/s

- The charged point conductor repels positive ions of the air while negative ions are attracted;(

The positive ions drift. Towards the flame forming an electric wind which drags the flame with it; 	(

- In X the vibrating air column produces a complete note or overtone with large amplitude while in Y, the vibration of air in test Y does not

- Infrared rays

- (i)	Easy to magnetize ((

(ii)	- Increasing the amount of current in the electromagnet ((

- Increasing the number of turns in the electromagnet. ((

N/B: Use the students drawing, if correctly drawn, to obtain the values of r and f by measuring.

- Camera does not have iris to control amount of light as in the eye.

Pinhole no lens while eye as a lens

- Easily magnetised& demagnetized

- Compare charges

- Detect charge

SECTION B 55 MARKS

- a)	That which opposes the flow of electrical current.

b) i)	Parallel ⇔1/R = 1/3 + 1/4

= 4 +3 = 7/12

12

R = 12/7

Series 12/7 + 2 = 12 + 14

7

= 3.86

ii)	V = 1R

⇔ 12 = I x 3.86

I = 12/3.86A

iii)	Through 4 resistor

= 3/7 of total

= 3/7 x V/R

= 3/7 x 12 x 7 A

= 1.38A

E = Pt = VIt

= 12 x 1.38 x 2 x 60J

= 1987.2J

d)	Radio circuit

Heater coils

Bulb filament

- a) i)	A device to store    charge

ii) Ability of a capacitor to store   charge.

b) i)Series1/c = 1/4 + 1/5 = 5 + 4 = 9/20

20

Parallel c = 20/9 + 3 = 20 + 9 = 29/9f

9

= 3.2 x 10-6F

ii)	Q = cv

= 29/9 x 10-6 x 10

= 32.2 x 10-5C.

c)	- Type of dielectric material

- Overlapping cross sectional area

- Distance between the plates

- a)	i)	Hard  X - rays(1

ii)	Have high penetrating power(1

b)	i)	A = Cathode rays( / fast moving electrons

B = Anode(1

ii)	 Change in heating current(1 changes the number of electrons produced(1

iii)	Kinetic energy(1 of cathode rays is converted to heat(1 energy.

iv)	Has high density (1

c)	eV = hf(1

1.6x 10-19 x 12000 = 6.62 x 10-34 x f (1

f  =

f =  2.9 x 10 18 Hz(1

- (a)

(b)  During the first half –cycle D1 is forward biased while D2 is reverse biased. Hence , current

takes the path A , D1 RT .√

During the next half –cycle, D2 is forward biased while D1 is reverse biased and the path of

the current is BD2RT.√

(c)  - Protects a circuit from damage  √

-  As a switch	√ Any 2

- In charging a battery using solar panels.

- (a) atomic number 90√1mark mass number 234√1mark

(b) (i) gamma rays.√1mark

(ii)  A are β particles which are negatively charged hence attracted to positively charged

plate and  are lighter than C hence more deviation compared to C which are α particles

which are positively  charged  hence attracted to the negatively charged plate and are

heavier  hence less deviation.

(c)

| correct account | 1018 | 964 | 896 | 808 | 689 | 527 | 300 |
| --- | --- | --- | --- | --- | --- | --- | --- |

(i)

(ii)

(iii)    half-life = 5.1min

# Text boxes

Rays = 2mks

f – ½ mk

r – ½ mk

Radius = 14.0cm

Rays = 2mks

f – ½ mk

r – ½ mk

F = 7.0cm

Radius = 14.0cm

(