Name…........................................................................................................................................

Index No……………………………School……………………………………………………

Date………………………………….Signature…………………………………………………..

448/1

ELECTRICITY

(Theory)

Paper 1

Time: 2 ½ hours

December 2021

BUNAMFAN CLUSTER EXAMINATION 2021

448/1

ELECTRICITY

(Theory)

Paper 1

Time: 2 ½ hours

December 2021

INSTRUCTIONS TO CANDIDATES

Candidates should have the following for this examination

- Mathematical tables or non-programmable calculators maybe used

- This paper has TWO sections: A and B

- Answer ALL the questions in section A and ANY FOUR questions from section B.

- All dimensions are in millimeters unless stated otherwise.

- This paper consists of 11 Printed pages.

- Candidates should check the question paper to ensure that all the Papers are printed as indicated and no questions are missing

This paper consists of 9 Printed pages.

Candidates should check the question paper to ensure that all the

Papers are printed as indicated and no questions are missing

SECTION A (48 MARKS)

Answer all the questions in this section.

- (a) State three safety precautions to be observed when using electric power tools. 	(1 ½ marks)

………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………

(b) State three requirements for proper storage or electrical measuring instruments. (1 ½ marks)

………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………

(c) Arrange the following job titles in ascending order of seniority: craftsman, engineer, artisan

and technician.									      (2 marks)

………………………………………………………………………………………………………………………………………………………………………………………………………………

- (a) Name two electrical equipment at the consumer’s intake point in a domestic installation.												      	       (1 mark)

………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………

(b) Explain each of the following electric circuit conditions.				       (2 marks)

(i) Short circuit

………………………………………………………………………………………………………………………………………………………………………………………………………………

(ii) Overload

………………………………………………………………………………………………………………………………………………………………………………………………………………

- State the effect of each of the following on current in an electric circuit. 	    	     (2 marks)

(i) Resistance

………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………

(ii) Inductance

………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………

- (a) Give two reasons why aluminum is preferred to copper for overhead power line cables. 													      (2 marks)

………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………

(b) In a 12V dc system a 40W solar panel is exposed to the sun for 6 hours daily. Calculate

the  number of days it will take to fully charge a 60 Ampere-hour battery. 	     (3 marks)

- (a) Describe the energy conversion sequence in a hydro-electric power station.     (2 marks)

………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………

(b) An alloy wire whose diameter is 1.0mm and resistivity is 75µΩm is used to make a 150Ω

resistor. Calculate the length of the wire. 					        (4 marks)

- (a) Name any two metals used to make alloy magnets. 				          (1 mark)

………………………………………………………………………………………………………………………………………………………………………………………………………………

(b) Explain how a permanent magnet can be demagnetized electrically. 		        (2 marks)

………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………

- (a) Explain why electric power is transmitted at high voltages. 			       (2 marks)

………………………………………………………………………………………………………………………………………………………………………………………………………………

(b) Explain the three functions of a switch gear at a domestic consumer’s intake point.													(3 marks)

………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………

- (a) Name one material used to make each of the following parts of electric machines:

(2 marks)

- Commutator segments	……………………………………………………………

- Slip rings			………………………………………………………………

- Brushes			………………………………………………………………

- Armature core			………………………………………………………………

- With respect to dc motors, explain the risk involved in each of the following malpractices:

(i) Switching the motor to directly to full supply voltage. 				        (3 marks)

………………………………………………………………………………………………………………………………………………………………………………………………………………

(ii) Running series motor without a load

………………………………………………………………………………………………………………………………………………………………………………………………………………

(iii) Operating a shunt motor while its field winding is open.

………………………………………………………………………………………………………………………………………………………………………………………………………………

- A moving coil instrument of internal resistance of 100 requires a current of 0.5mA to give 	full-scale deflection. If the instrument is modified to a voltmeter. Calculate the value of the 	multiplier for the instrument to measure up to 100V.					(3 marks)

- The figure 1 below shows an arrangement of capacitors connected to a 10V d.c supply.

Figure 1

Determine

- The combined capacitance							(2 marks)

- The total charge in the circuit							(1 mark)

- The total energy stored in the circuit.						(2 mark)

SECTION B (52 MARKS)

Answer any four questions from this section.

- (a) Explain why a series motor develops high torque when subjected to a heavier load.

(5 marks)

……………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………….…………………………………………………………………………………………………………………………………………………………………………………………

(b) A 240V/120V, 1.2kVA transformer delivers power to a load. Calculate the:

(i) Transformation ratio; 								(1 mark)

(ii) Rated secondary current;							(2 marks)

(iii) Primary impedance at the rated load;						     (3 marks)

- Number of turns in secondary winding if the primary winding induces 0.2V per turn.											      (2 marks)

- (a) Sketch the voltage-current characteristic curve of a rectifier diode and label:

- The axis

- VF

- VR

(b) Figure 2 shows a Zener diode regulator circuit.

Figure 2

- Given that the power dissipated by RS=2.125W, calculate the value of

- RS

- RL

- Power dissipated by RL

- If VIN is decreased to 11V, state what changes occurs in. 			        (9 marks)

- VR

- IZ

- (a) Using a well sketched diagram show the symbols of the following logic gates.    (2 marks)

- AND gate

- NOR gate

(b) Show the truth tables of the gates indicated below.				        (4 marks)

- NAND

- OR

(c) (i)  State any three considerations one has to make before settling for a certain business 			      idea.									(3 marks)

………………………………………………………………………………………………	………………………………………………………………………………………………	………………………………………………………………………………………………	………………………………………………………………………………………………	………………………………………………………………………………………………	………………………………………………………………………………………………

(ii) Explain the purpose of each of the following features in the circuit in (b) (i) above.

- Choke									     (2 marks)

………………………………………………………………………………………	………………………………………………………………………………………	………………………………………………………………………………………

- Fluorescent powder. 							        (2 marks)

………………………………………………………………………………………			………………………………………………………………………………………			………………………………………………………………………………………

(a) Figure 3 shows an ac RC circuit.

Figure 3

- Calculate the equivalent capacitance in the circuit. 			(2 marks)

- If at a frequency f, the reactive capacitance of the circuit is 6.0kΩ, calculate the magnitude of the current in the circuit.					(5 marks)

(b) Figure 4 shows an incomplete circuit of a full wave rectifier.

Figure 4

  - Draw in the figure two more diodes to complete the circuit. 			(2 marks)

  - Show on the circuit two points across which the rectified output should be obtained.											(2 marks)

  - State with reason the type of transformer shown above. 			(2 marks)

………………………………………………………………………………………………	………………………………………………………………………………………………	……………………………………………………………………………………………...

15.	(a)  Differentiate between an Ohmic and non-ohmic conductor giving one example in each case.													        (2 marks)

………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………

(b) Figure 5 shows a circuit with resistors and voltmeter connected to a battery.

Figure 5

- If each cell has an internal resistance of 0.7Ω, determine the total resistance in the circuit. 												     (3 marks)

- What amount of current flows through the 3Ω resistor when the switch is closed? (3 marks)

- What is the reading of the voltmeter when the switch S is

- Open									         (1 mark)

(II) 	Closed									      (1 mark)

- Account for the difference between the answers in (I) and (II) above. 	      (1mark)

………………………………………………………………………………………………	………………………………………………………………………………………………	………………………………………………………………………………………………

(c) State one environmental effect of setting up a diesel run power station. 		        (1 mark)

………………………………………………………………………………………………………………………………………………………………………………………………………………

LAST PAGE