PHYSICS PAPER 1

SECTION A (25 MARKS)

- 7.64mm

- Mass of water = 80-55

= 25g√

Vol of water = mass = 25	=25cm3 = volume of the bottle

P         1

Mass of liquid x =        70-55

=	15g

Density of x = mass of x √

Vol of the density of the

= 15g = 0.6g/cm3√ or 600kg/m3√

25cm3

- Pressure applied to an enclosed fluid is transmitted undiminished to every point in the fluid 	and to the walls of the container.(1

(b)

(1(1

- Diffusion will be faster in the beaker containing ethanol. This is because ethanol is less denser 	than water and diffusion is faster in a less dense medium.(1(1

- The wooden part tilts upward or the metallic part tilts downwards (any correct)

Reason

The metal part expands on heating becomes  longer thus the c.o.g shifts to the left

- Terminal velocity of water is very low(1

- Pressure increases with depth √1 The walls are thicker to withstand the greater force due to the increased pressure √1  to have maximum pressure, it should lie on minimum area ie. 3x6 cm2 √1

- W = mg

= 8kg x 10N/kg

= 80N ü1

Area = 10 x  5   = 0.005m2

100   100

P = F =     80N

A      0.005m2   ü1

= 16000N/m2 = 16000Pa ü1

- Total Clockwise moments =  total anticlockwise moments(1

17 x y  = 6(15) + 4.6 (10)

17y = 90 + 46

17y = 136

Y =8kg

Hence weight = 80N

- A1V1 = A2V2

48 x 10-4 x 10 = 12 x 10-4V2 ü1

V2 = 48 x 10

12

= 40m/s ü1

- h1p1g = h2p2g (

h1 : h2		= 	p2 : p1(

0.8 : 0.5	=	8 : 5(

SECTION B(55 marks)

- (a) (i) Mechanical advantage is defined as the ration of load to effort(1

(b) (i) V.R = 4 (1

(ii) Efficiency = M.A

V.R

M.A = V.R x efficiency(1

= 4 x 75/100

= 3(1

(iii) M.A = Load

Effort (1

Effort = Load = 2400 = 800N(1

M.A	      3

(iv) Efficiency = work output

Work input(1

Work imput = work output = 1200 x 2.5 (1

Efficiency	   0.75

= 4000J(1

(c) – Some energy is lost due to the frictional force between the parts of the machine.(1

- Some energy is used in lifting the parts of the machine(1

14. a)	The ball has the same horizontal velocity as the truck

b)	Impulse is equal to change in momentum

c)	m1u1 + m2u2 = v(m1 + m2)Vü1

30,000 x 20 + 0 = V(30,000 + 10,000)

V = 600,000 ü1

40,000

V = 15m/s ü1

ii)	S 	= Vt

= 15 x 15

= 225m ü1

iii)	Ft = m(v - u)

t

= 30,000 (20 - 15)

0.5

15.

(a)

(1

(1

= 1.49 x 106 Pa(1

(b)	(i)

| Pressure (atmosphere) | 1 | 1.3 | 1.5 | 1.8 | 2.3 | 2.6 | 3.2 | 3.7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Length of air column, L (mm) | 41 | 30 | 27.5 | 22 | 18 | 16 | 42.5 | 11.0 |
| 1/L x 10-2 (mm-1) | 2.44 | 3.33 | 3.64 | 4.55 | 5.56 | 6.25 | 8.00 | 9.09 |

(1 – 4) (1mk		(4 – 8) (1mk

(ii)

16. (a)	(i) OA – Increasing velocity or acceleration (1

(ii)     AB – Constant velocity(1

(b)

v = u + at

0 = 50 – 2t

t = 25s(1

(1

s = 625m(1

OR

v2 = u2 – 2as(1

2as = u2 – v2

(1

s = 625m

(c)	Initial ke = ½mv2

= ½ x 50 x 10 x 10

= 2500J

Double ke = 2500 x 2

= 5000J(1

5000 = ½mv2 (v = final velocity)

(1

F = ma

15 = 50a

(1

v = u + at

14.142 = 10 + 0.3t

(1

17.  a)	At high altitude atmospheric pressure is 	low, so boiling point is low. A pressure cooker increases pressure inside it which raises the boiling point hence faster cooking

b)	i)Heat absorbed by water = MCDq

= 3 x 4200 (100-20)X

= 1,008,000J ü1

ii)	Heat absorbed by kettle = CDq

= 450 x (100 - 20)

= 36000J

iii)	Time taken for water to boil

= Pt = mcDq + CDq

3000t = 1008000 + 36000

t = 1044000 ü1

3000

= 348s ü1

iv)	Q = mLv

= 3 x 2.3 x 106J

= 6.9 x 106 Jü1

Q = Pt

6.9 x 106 = 3000 x t

t = 6.9 x 106 = 2300

3000

t2 - t1 = 2300 - 348

=1952s