MANGU HIGH SCHOOL TRIAL 2 MOCK 2021

232/1 – PHYSICS PAPER 1 - MARKING SCHEME

- Actual reading 	= (6.20 – 0.02)mm

=	6.18mm(1

- h, ℓ, g = h2p2g(1

h x 900 = 0.06 x 1200(1

h = 0.08m = 8cm(1

- 4N

(1

Resultant force(1 = (10 – 6)N = 4N(1 towards the(1 right hand side.

- ℓ100 – ℓ0 = 30cm

Ф 	=	ℓ0 – ℓ0   	=	12

100		ℓ100 – ℓ0 		30

Ф 		=	12 x 1000C(1	=	400C(1

30

- Mass flux = density x volume flux(1

=	1000 x 160 x 10-6

=	0.16kgs-1

- In liquids the forces are smaller and molecules are able to roll(1 over one another while in the gaseous state, the molecules are free to move because gases have the weakest force(1 of attraction.

- A(1 – loses heat through evaporation because of large surface area and B(1 – because dull surface is a good emitter of heat. (1

- Lowered(1

As the water fills the vessel the centre of gravity rises and this lowers stability. (1

- It means a cubid centimeter of water has a mass of 1g. (1

- V.R.	=	R (Radius of the wheel)

r (radius of the axle

- Increase the radius of wheel (R)

- Reduce the radius of the axle (r)

- (a)  in a vacuum

(b)

Combined spring constant S1, S2, S3 = 3x5N/m		OR

=	15N/m		S1, S2, S3

L + 20

e 	=	F				    3

K				5N = 1m

(28 – e)	=	(L + 20)			L + 20 = ?

15				   3

420 – 15e	=	L + 20				(L + 20) (1

15

400 = L + 15e … (i)					5N = 1m

L = ?

e	=	L				L(1

K				5

e	=	L				Therefore L + 20 + L = 28

5					         15       5

5e	=	L … (ii)			L + 20 + 3L = 420

4L = 400

simultaneously (i) and (ii)				L = 100(1

e 	=	400

20

=	20m

Therefore 	L	=	5 x 20

100N(1

- (a)  Vertical projection U = 100m/s g = -10m/s v = om/s

V2 = u2 – 2gs(1

O2= (100)2 – 2 x 10 x 5

20s = 10,000

s = 500m(1

(b)  Horizontal projection h = ½ gt2(1

500 = ½ x 10 x t2

t2 = 100

t = 10s(1

(c)  Range	R = ut(1

R = 20 x 10

= 200m(1

(d) Impulse	=	change in momentum(1

Ft 		=	(10N x 35)(1 – (20N x 25)

=	-10NS(1

(e) (i)  v – u 	=	a

t

t 	=	(5 ticks x 0.01)s

=	0.05s(1

Therefore	  Δv	=	5cm/s2

0.05

Δv	=	0.25cm/s(1

(ii)  v – u 	=	0.25cm/s

u	=	0.125cm

0.01

=	12.5cm/s(1

V – 12.5 = 0.25

V = 12.75cm/s(1

- (a)  (i)  M.A = 	L

E

=	450N(1

150N

=	3(1

(ii) V.R = No. of teeth on driven gear

No. of teeth on driving gear

=	80(1

20

=	4

(iii) ŋ	=	m.A x 100%

V.R

=	¾ x 100%

=	75%

(b)  (i)  Converts electrical energy – sound energy. (1

(ii)  Chemical		Kinetic	Potential

(c)  Mass of ice	=	0.9g/cm3 x 2000cm3

1800g

1.8kg

+0.2

2.0kg(1

w = Fxd

=	20N x 5M

=	 100J(1

Power	=	Work done

Time

=	100J

4S

=	25J/S or 25 watts(1

- (a)  Quantity of heat required to convert a unit mass of liquid to vapour at constant temperature. ( (2mks)

- Mass of condensed steam 	= 	123 – (70 + 50)			(1mk)

=	123 – 120 = 3g			(1mk)

(ii) Heat gained by water 		=	MCΔQ

=	0.07 x 4200 x 25 = 7350J

Heat gained by cal 		=	  50    x 390 x 25 = 487.5J

1000					(1mk)

Total heat gained		=	487.5 + 7350 = 7837.5J		(1mk)

(iii)  (i)  Heat lost by steam 		=	ml + MCΔE

=  0.003l + (0.003 x 4200 x 70) = 7837.5J

0.003L = 6955.5

(ii) L = 6955.5

0.003

= 2318500J

- (i)  At P = 2.5 x 105Pa, I/V = 50m-3(read from graph)

Therefore V = 1/50 = 0.02m3(1

(ii) Gradient = 2RT		grad	=	 3 – 2	=	1	=	0.05

60 – 40	20

R 	=	gradient

2T

R	=	  0.05		=	8.3 x 105N m/k or JK-1(1

2x 300

- (a)  Floating object displaces its own weight of the fluid in which it floats.

(b)  Mass of water displaced by wood = 80kg

Volume of water displaced 	=	  80	=	0.08m3

1000

but 0.08m3 = 0.6 of the volume of block.

Volume of wood = 0.08	=	0.1333m3;

0.6

Volume displaced by rods	=	0.08 – 0.1333 = 0.0533

Mass of he rods = 0.053 x 1000 = 53.3kg;

Mass of one rod = 20g = 0.02kg

Number of rods	=	53.3;

0.02

=	2,665 rods;

- (i)  Up thrust force

Weight			((Max. 2 or 3;;

Tension on the string		1

Up thrust = weight + tension on the string;

(ii)	Up thrust	=	weight + tension

(50 x 40 x 20) 1000 x 10 = 50 x 40 x 20 x 6000 + tension;;

1000000			       100000

Tension = 200 – 240

=	-40N

- Sum of clockwise Moments = Anti clockwise Moments(1

37.5 x 40 + W x 40 = 140 x 15

1500 + 40W = 2100

40W = 2100 – 1500

40W = 600

W = 6N(1

W = 15N

M = 1.5Kg or 1500g

- (a)  (i)  Roughness( / smoothness( of surface / radius of path / angular velocity /

speed.								(any two)

(ii) WA > WB > WC(1